## Slide 1: Lecture 4,5

## Slide 2: Program and Network Properties
Fundamental properties of program behavior
Major classes of interconnection network
Computational granularity
Condition for program partitioning
Matching software with hardware
Program flow mechanism
Compiler support for parallelism

## Slide 3: Condition of Parallelism
Need to make significant progress in 3 key areas.
  Computation models for parallel computing
  Interprocessor communication
  System integration for incorporating parallel system into general computing environments

## Slide 4: Data and Resource Dependences
To execute several program in parallel requires each segment to be independent of the other segment
Dependence graph describe the relation
  Node correspond to the program statements
  Edge show the ordered relation among statements.
  Analysis of dependence graph shows where opportunity exists for parallelization

## Slide 5: Data Dependence
Ordering relationship between statements indicated by data dependence
  Flow dependence: Statement S2 is flow dependent on statement S1 if an execution path exists from S1 to S2 and if at least one output of S1 feeds in as input to S2. Denoted by S1→S2

## Slide 6: Data dependence example
S1: Load R1, A
S2: Add R2, R1
S3: Move R1, R3
S4: Store B, R1
S1
S2
S4
S3

## Slide 7: Data Dependence (cont..)
Antidependence: S2 follows S1 and if the output of S2 overlaps the input to S1
Output dependence: if two statement produce or write the same output variable
I/O dependence: Is same file is referenced by both I/O statements

## Slide 8: Example
S2 is flow dependent to S1
S3 is antidependent on S2
S3 is output dependent on S1
Not every pair of statement are related (Partial ordering relation)
S2 and S4 totally independent
S1: Load R1, A
S2: Add R2, R1
S3: Move R1, R3
S4: Store B, R1

## Slide 9: Example (2)
S1 and S3 are I/O dependent
S1: Read (4), A(I)
S2: Rewind (4)
S3: Write (4), B(I)
S4: Rewind (4)

## Slide 10: Control Dependence
The order of execution of statement cannot be determined before run time
  E.g. Conditional statement will not resolved until run time
Dependence may also exist between operation performed in successive iteration of looping procedure

## Slide 11: Example
For( i=0; i <N ; i++) { A[i]=C[i]; If(A[i]<0) { A[i]=1; } } | For( i=1; i <N ; i++) { If(A[i-1]==0) { A[i]=0; } }
Control Independent | Control Dependent

## Slide 12: Resource Dependence
Concerned with the conflicts in using shared resource (e.g. int unit, floating unit, registers, memory etc.)
When conflicting resource is ALU, it is called ALU dependence
Storage dependence
Transformation of sequentially coded program into parallel executable form can be done by explicit or implicit parallelism
The detection of parallelism requires a check of the various dependence relation

## Slide 13: Bernstein’s Conditions
Set of conditions which determines which two processes can execute in parallel
Process P1 and P2 can execute in parallel if they are independent and do not create confusing results
Denotes as P1||P2

## Slide 14: Bernstein’s Conditions (cont..)
Conditions are states as follows
I1 ∩ O2 = Null
I2 ∩ O1 = Null
O1 ∩ O2 = Null
I1, I2 are input sets of P1 and P2
O1, O2 are output sets
Simply imply that two processes can execute in parallel if they are flow independent, antindependent and output independent.
A Set of processes, P1, P2 ……… Pk can execute in parallel if Bernstein’s conditions are satisfied on a pair wise basis.
That is Pi||Pj if for all i≠ j

## Slide 15: Example
10 pairs of statement to check against Bernstein’s Condition
P1||P5, P2||P3, P2||P5, P5||P3 and P4||P5 can execute in parallel
|| relation is commutative
Not transitive
P1: C = D * E
P2: M = G + C
P3: A = B + C
P4: C = L + M
P5: F = G / E

## Slide 16: Hardware Parallelism
Function of Cost and performance tradeoffs
One way to characterize the number of instruction issues per machine cycle
If a processor issues k instruction per machine cycle then it is called a K-issue processor.
A conventional processor takes one or more machine cycle to issue a single instruction.
Modern processor issue more instructions.
A multiprocessor system built with N K-issue processor which can handle NK threads of instructions simultaneously.

## Slide 17: Software Parallelism
Defined by the control and data dependence of programs.
Is a function of algorithm, programming, and compiler optimization.

## Slide 18: Software and Hardware Parallelism

## Slide 19: Software and Hardware Parallelism
L1
L2
L3
L4
X1
X2
+
-
C1
C2
C3
C4
C5
C6
C7

## Slide 20: Mismatch between s/w and h/w parallelism

## Slide 21: Software parallelism
Control parallelism – allows two or more operations to be performed concurrently
  Pipelining, multiple functional units
Data parallelism – almost the same operation is performed over many data elements by many processors concurrently
  Code is easier to write and debug

## Slide 22
Program Partitioning & Scheduling

## Slide 23: Grain sizes and latency
Granularity is a measure of the amount of computation involved in a software process
  Count the number of instructions in a segment
  Fine, medium, or coarse
Latency is a time measure of the communication overhead
  Memory or synchronization latency

## Slide 24: Levels of parallelism
Instruction level (fine)
Loop level (fine)
Procedure level (medium)
Subprogram level (medium to coarse)
Job or program level (coarse)

## Slide 25: Communication latency
Latency imposes a limiting factor on the scalability of the machine size
Memory Latency Increase with respect to memory capacity.
Communication patterns are determined by the algorithms used and by the architectural support provided
  Permutations, broadcast, multicast, and conference

## Slide 26: Grain packing and scheduling
The grain size problem requires determination of both the number of partitions and the size of grains in a parallel problem
Solution is problem dependent and machine dependent
Want a short schedule for fast execution of subdivided program modules

## Slide 27: Grain packing and scheduling

## Slide 28: Grain packing and scheduling

## Slide 29: Grain packing and scheduling

## Slide 30: Static multiprocessor scheduling
Grain packing may not be optimal
Dynamic multiprocessor scheduling is an NP-hard problem
Node duplication is a static scheme for multiprocessor scheduling

## Slide 31: Node duplication
Duplicate some nodes to eliminate idle time and reduce communication delays
Grain packing and node duplication are often used jointly to determine the best grain size and corresponding schedule

## Slide 32: Schedule without node duplication
A,4
a,1
b,1
c,8
a,8
c,1
C,1
B,1
D,2
E,2
e,4
d,4
P1
P2
P2
P1
A
D
B
I
E
C
I
4
6
13
21
27
23
20
16
14
12
4

## Slide 33: Schedule with node duplication
A,4
a,1
b,1
c,1
a,1
c,1
C’,1
B,1
D,2
E,2
P1
P2
P2
P1
A
D
B
E
C
A
4
6
10
14
13
9
6
4
C,1
A’,4
a,1
C
7

## Slide 34: Grain determination and scheduling optimization
Step 1: Construct a fine-grain program graph
Step 2: Schedule the fine-grain computation
Step 3: Grain packing to produce coarse grains
Step 4: Generate a parallel schedule based on
the packed graph

## Slide 35: Program Flow Mechanisms
Control Flow Computers
Data Flow Computers
Demand Driven Computers

## Slide 36: Control Flow Computers
Use shared memory to hold program instructions and data
Are inherently sequential due to the control-driven mechanism
Can be made parallel by using parallel language constructs and parallel compilers

## Slide 37: Dataflow Computers
Data availability drives the execution of instructions
Data tokens are passed directly between instructions
No shared memory, program counter or control sequencer

## Slide 38: Dataflow Computers (cont.)
Require special mechanisms to detect data availability
Require special mechanism to match data tokens with the instructions that need them
Require special mechanism to enable the chain reaction of asynchronous instruction executions.

## Slide 39: Demand Driven Computers (Reduction Computers)
The computation is triggered by the demand for an operation’s result
It uses a top-down approach
Instructions are executed only when other instructions need their results

## Slide 40: Reduction Computers Models
String Reduction Model: Each demander gets a separate copy of the expression for its own evaluation. A long string expression is reduced to a single value in a recursive fashion.
Graph Reduction Model: The expression is represented as a directed graph.The graph is reduced by evaluation of branches or subgraphs.

## Slide 41: System Interconnect Architecture
Static and dynamic networks for interconnecting computer subsystems or for constructing multiprocessors or multicomputers
Ideal: Construct a low-latency network with a high data transfer rate

## Slide 42: Network Properties and Routing
Static Networks: Point-to-Point direct connections which will not change during program execution
Dynamic Networks: Implemented with switched channels. They are dynamically configured to match the communication demand in user programs

## Slide 43: Network Parameters
Network size: The number of nodes in the graph used to represent the network
Node Degree d: The number of edges incident to a node. Sum of in degree and out degree
Network Diameter D: The maximum shortest path between any two nodes

## Slide 44: Network Parameters (cont.)
Bisection Width:
  Channel bisection width b: The minimum number of edges along the cut that divides the network in two equal halves
  Each channel has w bit wires
  Wire bisection width: B=b*w; B is the wiring density of the network. It provides a good indicator of tha max communication bandwidth along the bisection of the network

## Slide 45: Network Parameters (cont.)
Data Routing Functions: used for inter-PE data exchange. They can be static or dynamic
Common Data Routing Functions:
  Shifting
  Rotation
  Permutation (one-to-one)
  Broadcast (one-to-many)
  Multicast (many-to-many)
  Personalized Communication (one-to-many)
  Shuffle
  Exchange

## Slide 46: Permutations
For n objects there are n! permutations by which the n objects can be reordered.The set of all permutations form a permutation group with respect to a composition operation. Cycle notation can be used to specify a permutation operation.
Permutation p = (a, b, c)(d, e) means: a->b, b->c, c->a, d->e and e->d in a circular fashion. The cycle (a, b, c) has a period of 3, and the cycle (d, e) has a period of 2. p will have a period equal to 2 x 3 = 6.

## Slide 47: Permutations (cont.)
Can be implemented using crossbar switches, multistage networks or with shifting or broadcast operations.
Permutation capability is an indication of network’s data routing capabilities

## Slide 48: Perfect Shuffle
Special permutation function
n = 2k objects; each object representation requires k bits
Perfect shuffle maps x to y where:
  x = ( xk-1, …, x1, x0 )
  y = ( xk-2, …, x1, x0, xk-1 )

## Slide 49: Exchange
n = 2k objects; each object representation requires k bits
The exchange maps x to y where:
  x = ( xk-1, …, x1, x0 )
  y = ( xk-1, …, x1, x0’ )
Hypercube routing functions are exchanges

## Slide 50: Broadcast and Multicast
Broadcast: One-to-all mapping
Multicast: one subset to another subset
Personalized Broadcast: Personalized messages to only selected receivers

## Slide 51: Network Performance
Functionality
Network latency
Bandwidth
Hardware complexity
Scalability

## Slide 52: Static Connection Networks
Linear Array
Ring and Chordal Ring
Barrel Shifter
Tree and Star
Fat tree
Mesh and Torus
Systolic Arrays
Hypercubes
Cube connected cycles
k-ary n-Cube networks

## Slide 53: Dynamic Connection Networks
Digital Buses
Switch modules
Multistage networks
  Omega Network
Crossbar Networks